## Slide 1: PSAS Electric Propellant Feed System
Affiliations: 1Portland State Aerospace Society, 2Maseeh College of Engineering and Computer Science Portland, OR, 97201, United States

## Slide 2
The Team
Team Members (left to right):
Mimi Shang, James Luce, Jorden Roland, Johnny Froehlich, Johnathan Talik, Rawand Rasheed

## Slide 3
The Problem
Portland State Aerospace Society (PSAS) wants its rockets to go higher, but mass is the enemy:
Δv = change in velocity
Ve = exhaust velocity
mo = mass of rocket + propellant
mf = mass of rocket

## Slide 4
Past approach: solid propellant
Most small rockets use solid propellant.
Simple but inefficient.
Can’t throttle = can’t insert into orbit.
Images: http://www.fireworkssupermarket.com, http://www.aerospace.org
Solid propellant
Grain bore
Nozzle
Solid propellant rocket design
Solid propellant rocket example

## Slide 5
Liquid propellant
Gives more Δv for its mass = goes higher.
Can be throttled = can insert into orbit.
Images from wikipedia
Pressure fed: too heavy
Turbopump: too complex

## Slide 6
Tank
Turbopump without turbine = just a pump.
Battery energy density has been rising.
Lighter than pressure fed, simpler than turbopump.
https://en.wikipedia.org/
http://www.blue-sky-technologies.com/impeller-seal-repair/
https://www.digikey.com/
New approach: electric pump
Engine
Electric motor
Pump

## Slide 7
Project Goal
Goal:
Design a test pump to meet PSAS’ requirements.
Test with water (not cryogenic liquid oxygen and isopropyl alcohol).
Performance results will be scaled to design actual rocket pump.

## Slide 8
Customer Requirements
Pressure delivery | Must produce discharge pressures of 300-400 psi.
Flow capacity | Must supply a flow rate of ~12 gpm.
Transferability | Documentation must be open source and transferable to future PSAS engineers.
Off-the-shelf components | Must utilize off the shelf components wherever possible.
Cost | Project must be completed for less than $8000

## Slide 9
Open-ended literature review
Math is involved
Scientific computing
Some
assumptions
Getting started

## Slide 10
Getting started
Visualize the Results
You are here
Parametric Design
Viola!

## Slide 11
Pump regimes
Specific speed is a term used to describe the geometry (shape) of a pump impeller.
Our specific speed
Very Low
Low
?
?
?
?

## Slide 12
Searching for clues

## Slide 13
Searching for clues
Salient Features:
Semi-open impeller
Flow enters axially and exits radially
Casing is bored concentrically with impeller centerline
Fluid allowed to recirculate within the casing
Single emission throat
Conical diffuser oriented tangentially to the case bore
Final parameters of hydraulic structure

## Slide 14
Challenge: Fabrication
Head v. flow requirements meant commercially available pumps wouldn’t work.
Outsourcing fabrication would be cost prohibitive.

## Slide 15
Challenge: Precision
High speeds and loads with low tolerances meant fabrication had to be precise.
0.06” +/- 0.01”
+/- ~0.0007”
Impeller (cross section)

## Slide 16
Solution: Time investment
Designed parts around available fabrication techniques.
Learned 3-axis CNC mill and 2 axis CNC lathe.
Several thousand (wo)man hours in the shop.

## Slide 17
Solution: Time investment

## Slide 18
Solution: Time investment

## Slide 19
Solution: Time investment

## Slide 20
Challenge: Power measurement
We need to know the power applied to the fluid.
Hard to extract this data directly from motor.
Solution: live dynamometer.
motor
“floating” motor adapter
bearing
torque arm

## Slide 21
Subsystem structure
EFS Subsystems
Mechanical
Power
Flow Loop
Measurement
Hydraulic
Bearings
Seals
Shaft
Coupling
Alignment
Impeller
Diffuser
Volute
Supply Tank
Valves
Tubing
Arduino
Excel DAQ
Sensors
Motor
Batteries
ESC
Control

## Slide 22
Subsystem structure
Power
Hydraulic
Motor
Bearings
Seals
Shaft
Coupling
Alignment
Impeller
Diffuser
Volute
Mechanical

## Slide 23
Subsystem structure
Hydraulic
&
Mechanical
Power
Flow Loop
Measurement
Motor
Batteries
ESC
Control
Cooling
Impeller
Diffuser
Volute
Supply Tank
Valves
Tubing
Bearings
Seals
Shaft
Coupling
Alignment
Arduino
Excel DAQ
Sensors

## Slide 24
Characterizing the performance
Hydraulic Institute Test Standard (ANSI/HI 14.6)
Pump performance is given by:
• Head versus capacity
• Power versus capacity
• NPSH versus capacity

## Slide 25
System characteristics
Swamee-Jain Equation (1976)
Energy Equation
Explicit expression 10-6 < e/D, 10-2; 5000 < NR < 108

## Slide 26
Measurement
Optical sensor

## Slide 27
Our performance (16,500 rpm)
Figure: EFS model PIGLET-1 2.1in Diam. Impeller experimental results at 16500 rpm.

## Slide 28
Comparing impellers
Vs.
Z = 10
Z = 6
10 Blades
Slightly higher (~ 2 %) discharge pressures for a given flow rate.
6 Blades
Lower chamber pressures (~ 8 %)
Earlier run-out (lower max. flow)

## Slide 29
Meeting requirements
Customer Requirements

## Slide 30
Next steps
Thoroughly investigate existing water pump (impellers, diffusers, rpm etc.)
Modify water pump to learn more, if needed.
Scale design for PSAS needs and cryo application.
Hot fire test!
Launch!