## Slide 1: Electronic Propellant Feed System
Affiliations: 1Portland State Aerospace Society, 2Maseeh College of Engineering and Computer Science Portland, OR, 97201, United States
Johnny Froehlich, Jonathan Talik, James Luce, Rawand Rasheed, Mimi Shang, Jordan Roland

## Slide 2: The problem
Portland State Aerospace Society (PSAS) wants its rockets to go higher.
The rocket equation dominates:
Δv = change in velocity
Ve = exhaust velocity
mo = mass of rocket + propellant
mf = mass of rocket

## Slide 3: Past approach
Most small rockets use solid propellant.
Solid propellant is easy but inefficient.
Can’t throttle solid rockets= can’t insert into orbit.

## Slide 4: Liquid propellant
Liquid propellant gives more Δv for its mass.
Common approaches:
Images from wikipedia
Pressure fed: too heavy
Turbopump: too complex

## Slide 5: Electric motors: a new approach?
Remove the turbine from a turbopump = just a pump.
Battery energy density has been rising.
This is a new space in rocketry.
https://en.wikipedia.org/
http://www.blue-sky-technologies.com/impeller-seal-repair/
http://www.worldwideelectric.net/

## Slide 6
6
Portland State Aerospace Society | Electric Propellant Feed System
Notes: 6

## Slide 7
7
Open-ended literature review
Puzzle break
Scientific computing
We made some guesses too
Notes: 7

## Slide 8
8
Map out predictions
You are here
Play with the design
Create something
Notes: 8

## Slide 9: #5 Final Design and Subsystem breakdown
Delete slide before inserting into active

## Slide 10
Portland State Aerospace Society | Electric Propellant Feed System
Final Design: Review
To insert:
Flow diagram of testing apparatus – Diagram
Actual Testing Assembly – High res photo
Notes:
look at the thing we created: a testing and development platform for an electric feed system

## Slide 11
Electric Feed System
Pump
Casing
Hydraulic
Mechanical
Bearings
Seals
Drive
Motor
Control
Batteries
Dyno Mount
Testing
Flow Loop
Flow Loop
Air Pressure
Water
Seals
Measurement
Pressure
Flow
RPM
Torque

## Slide 12
Portland State Aerospace Society | Electric Propellant Feed System
Final Design: Subsystem
To insert:
Quarter section – CAD
Photo of the pump w/ casing – High Res
Notes:
Subsystem breakdown:
Pump:
  Bearing system
  Seal system
  Hydraulic system ( volute, impeller, diffuser) – highlight modular design
  Shaft

## Slide 13
Portland State Aerospace Society | Electric Propellant Feed System
Final Design: Review
To insert:
WIT
SECTION VIEW
Notes:
Hydraulic design
Structure parameters of EFS partial emission pump |  |  |  | 
Discription |  |  | Value | 
Impeller Outlet Diameter D2(in) |  |  | 2.1 | 
Impeller Blade width b2(in) |  |  | 0.2 | 
Discharge Throat Diameter D1(in) |  |  | 0.18 | 
Impeller eye Diameter De(in) |  |  | 0.43 | 
No. of Blades |  |  | 10 | 
Impeller Discharge Angle β(̊) |  |  | 36 | 
Base Diameter of Volute Caseing D3(in) |  |  | 2.42 | 
Length of Diffuser section LD(in) |  |  | 1.2 | 
Diffusion Angle α(̊) |  |  | 8 | 
Performance parameters of EFS partial emission pump |  |  |  | 
Discription |  |  | Value | 
Q (G.P.M) |  |  | 12 | 
H (ft) |  |  | 754 | 
Nr (r/min) |  |  | 20500 | 
P (KW) |  |  | ≤ 3.5 | 

## Slide 14
Portland State Aerospace Society | Electric Propellant Feed System
Final Design: Subsystem
Motor Dynamometer Mount
Notes:
Subsystem breakdown:
Drive:
  Motor / esc / battery / control
  Motor Dyno mount (floating torque measurement)
  Motor coupling – Alignment and verifying runout (angular / offset)
To insert:
Rendering of the motor dyno – CAD
Photo or diagram of the motor

## Slide 15
Portland State Aerospace Society | Electric Propellant Feed System
Final Design: Subsystem
Motor Mounting and Control
Notes:
Subsystem breakdown:
Drive:
  Motor / esc / battery / control
  Motor Dyno mount (floating torque measurement)
  Motor coupling – Alignment and verifying runout (angular / offset)
To insert:
Rendering of the motor dyno – CAD
Photo or diagram of the motor
R
L
T

## Slide 16
Portland State Aerospace Society | Electric Propellant Feed System
Final Design: Subsystem
To insert:
Flow diagram of testing apparatus – Diagram
Photo of the testing apparatus – high res photo
Photo of DAQ / measurement / harness
Notes:
Subsystem breakdown:
Testing Apparatus:
  Tank, suction line, discharge, experimental procedure, cooling
  Sensing
  Pressure, flow, RPM, Torque
  Data Acquisition
  Arduino to excel
Currently not in use….

## Slide 17: Challenges / Solutions: Fabrication

## Slide 18
Challenge: Fabrication
Head v. flow requirements meant commercially available pumps wouldn’t work.
Outsourcing fabrication would be cost prohibitive.

## Slide 19
Challenge: Precision
High speeds and loads with low tolerances meant fabrication had to be precise.
0.06” +/- 0.01”
+/- ~0.0007”

## Slide 20
Solution: Time investment
Designed parts around available fabrication techniques.
Learned 3-axis CNC mill and 2 axis CNC lathe.
Several thousand (wo)man hours in the shop.

## Slide 22
Portland State Aerospace Society | Electric Propellant Feed System
Challenges
Notes:
2. Controls / Measurement
Problems:
Motor control
Sensing and measurement for performance curves
Solutions:
Quad Copter rigging / controller potentiometer tricking
Sensors
Arduino DAQ
To insert:
Photo, highlight sensors
Photo, DAQ
Photo, Motor control

## Slide 23
Notes:
Unfinished pieces:
more robust (safe) controls system
more variation of impeller geometry
a method of manufacturing diffusers that can be extended to a lox design
What you learned:
we overbuilt the hell out of this pump
What should be done next:
Full suite of testing to inform the next design decisions.
optimize seals bearing and material selections for cryo/Lox
v2 ready for hot fire testing.

## Slide 24
Unfinished Business: Controls and Safety
More robust (read safe) controls system
  Clean up wiring
  Either a dedicated transmitter set up or hard wired throttle control
  Replace all gauges with data

## Slide 25
Unfinished Business: Lessons
Pump is over-designed but for a reason

## Slide 26
Next steps:
Full suite of testing
Design it for really fucking cold
Make FIRE!!!!